## Slide 1: F5 Monitoring & Reporting
Chas Lesley
Field Systems Engineer
Tony Ganzer
Territory Account Manager

## Slide 2
If a tree falls in the forest and no one is watching does it make a noise?

## Slide 3
If a system fails in the network and no one is watching does it make a noise?

## Slide 4
ABSOLUTELY!!!

## Slide 5
We don’t know everything,
Everyone needs to contribute.
Every environment is at different levels

## Slide 6: General Warning
IMPORTANT:
The BIG-IP system has many capabilities, functions and features. Avoid testing capabilities, functions and features or new concepts, confiugrations or designs on production systems unless the potential impact is understood and acceptable.
As with any tool, understand it before you use it
Liability Release Complete

## Slide 7
SNMP
Logging
sFlow
AddOns
Accounting, Visibility
& Reporting
Agenda
Cover general SNMP setup & configuration
Review some of the available logging options
Quick overview of function & configuration
Quick look at integrations (Splunk)
Deeper dive into AVR & capabilities
iControl
Skunk Works

## Slide 8
SNMP
Logging
sFlow
AddOns
Accounting, Visibility
& Reporting
iControl
Skunk Works

## Slide 9
SNMP
Agents
Traps
System
https://support.f5.com/kb/en-us/products/big-ip_ltm/manuals/product/bigip-external-monitoring-implementations-11-6-0/11.html#conceptid
Notes: Monitoring BIG-IP System Traffic with SNMP: https://support.f5.com/kb/en-us/products/big-ip_ltm/manuals/product/bigip-external-monitoring-implementations-11-6-0/11.html#conceptid

## Slide 10
SNMP Setup - Agents
Restrict access by IP
Read Only
Read/Write
Access (v1, v2c)

## Slide 11
SNMP Setup - Agents
Access (v3)
Read Only
Read/Write
MD5
SHA
None
AES
DES
None

## Slide 12
SNMP Setup - Traps
V1
V2c
V3
Agent Start/Stop:
Specifies, when checked (enabled), that the system sends a trap whenever the SNMP agent starts running or stops running. The default is enabled.
Agent Authentication:
Specifies, when checked (enabled), that the system sends authentication warning traps to the trap destinations. The default is disabled.
Device:
Specifies, when checked (enabled), that the system sends device warning traps to the trap destinations.
SNMP Trap Source Interface
Notes: SNMP Trap Source Interface: https://support.f5.com/kb/en-us/solutions/public/7000/500/sol7530.html
Management Interface Routing: https://support.f5.com/kb/en-us/solutions/public/13000/200/sol13284.html

## Slide 13
SNMP - MIBs
Overview of MIB Files: https://support.f5.com/kb/en-us/solutions/public/13000/300/sol13322.html

## Slide 14
snmpwalk -v 2c -c public localhost bigipLocalTM
SNMPWalk (CLI) - Testing
Solution Article
Notes: SNMPWalk: https://support.f5.com/kb/en-us/solutions/public/6000/700/sol6774.html
snmpget -c public 192.168.69.245 sysGlobalStat.sysStatMemoryUsed.0
snmpwalk -v2c -c public localhost hrSWRunName | egrep "\"tmm(.[0-9]+)?\"" | wc -l

## Slide 15
Installation Instructions
http://www.opennms.org/wiki/Installation:Yum
SNMP – NMS
Notes: http://www.opennms.org/wiki/Installation:Yum
http://www.postgresql.org/download/linux/redhat/
rpm --import http://yum.opennms.org/OPENNMS-GPG-KEY
yum -y install opennms

## Slide 16
SNMP
Logging
sFlow
AddOns
Accounting, Visibility
& Reporting
iControl
Skunk Works
Notes: Managing Log Files: https://support.f5.com/kb/en-us/solutions/public/13000/300/sol13367.html

## Slide 17
Syslog
Output all system log information
Configurable with Options & Filters
Provides a historical repository (audit regulations and compliance)
High-Speed Logging
High Speed Logging was designed to be a high volume, low overhead logging mechanism. (<10% CPU)
Supports logging via TCP or UDP.
Log all HTTP requests & responses
Log the SSL cipher name, version, size for each session
Logging Local0.
Quick diagnostic evaluations
iRule troubleshooting & debugging
Did I say – EXTREMELY helpful in iRule Authoring!
Logging (a quick three…)
Notes: https://devcentral.f5.com/wiki/iRules.HSL.ashx?lc=1

## Slide 18
Logging – Syslog
( sol13080 )
SysLog Configuration: https://support.f5.com/kb/en-us/solutions/public/13000/000/sol13080.html
SysLog Filtering: https://support.f5.com/kb/en-us/solutions/public/13000/300/sol13333.html
Target IP
(syslog Server)
Syslog Server destination Port
Notes: SysLog Configuration: https://support.f5.com/kb/en-us/solutions/public/13000/000/sol13080.html
SysLog Filtering: https://support.f5.com/kb/en-us/solutions/public/13000/300/sol13333.html

## Slide 19
Logging – High Speed Logging (HSL)
https://support.f5.com/kb/en-us/products/big-ip_ltm/manuals/product/bigip-external-monitoring-implementations-11-6-0/2.html
Target a pool of logging servers
Address high speed logging needs
  Firewall Designs
  All HTTP Request/Responses
  Log all SSL Cipher information
“Replace” TCPDump (log decrypted content)
Notes: High Speed Logging: https://devcentral.f5.com/wiki/iRules.HSL.ashx?lc=1
Configuration: https://support.f5.com/kb/en-us/products/big-ip_ltm/manuals/product/bigip-external-monitoring-implementations-11-6-0/2.html
HSL: https://support.f5.com/kb/en-us/solutions/public/14000/400/sol14459.html
iRule: https://devcentral.f5.com/articles/irules-high-speed-logging-spray-those-log-statements

## Slide 20
Logging – local0. (iRules)
99% of all cases you will use
log local0. "message goes here"
What you will see in your Local Traffic Log files
Notes: https://devcentral.f5.com/articles/irules-101-09-debugging

## Slide 21
Logging – local0. (iRules - Debugging)
When done with logging statements you can
Delete
Comment out #
Add conditionals as shown with SET statements
1,2= No CPU hit
3= CPU hit depending on load

## Slide 22
SNMP
Logging
sFlow
AddOns
Accounting, Visibility
& Reporting
iControl
Skunk Works

## Slide 23
sFlow - Overview
sFlow “Sampled Flow” is an industry-standard technology for monitoring high-speed switched networks.
Netflow not supported
IPFIX supported (from Advanced Firewall Module (AFM)
As of 11.4 TMM interfaces are used (Prior to 11.4 mgmt. interface)
Flow Samples:
Based on a defined sampling rate, an average of 1 out of n packets/operations. (quantifiable accuracy)
Counter Samples
A polling interval defines how often the network device sends interface counters.
sFlow Datagrams
The sampled data is sent as a UDP (default port 6343)
( sol15193 )
Notes: https://support.f5.com/kb/en-us/solutions/public/15000/100/sol15193.html

## Slide 24
sFlow – Configuration (Receiver)

## Slide 25
dept1
Globally modify Polling interval and Sampling Rate packet/# of packets
Cannot modify interface or System Sampling rates
Modify individual data sources through HTTP profile or VLAN
  Polling Interval
  Sampling Rate
sFlow – Global Settings & DataSources

## Slide 26
sFlow Closer Look
Wireshark inMon
sFlow dissector

## Slide 27
sFlow – Collectors

## Slide 28
SNMP
Logging
sFlow
AddOns
Accounting, Visibility
& Reporting
iControl
Skunk Works

## Slide 29
AddOns (Integrations)
https://devcentral.f5.com/articles/getting-started-with-splunk-for-f5
Getting Started with SPLUNK https://devcentral.f5.com/articles/getting-started-with-splunk-for-f5
SPLUNK for APM
https://www.f5.com/pdf/solution-center/splunk-templates-for-apm.pdf
SPLUNK for ASM
https://www.f5.com/pdf/solution-center/splunk-asm-sb.pdf
SPLUNK Apps (extensions for F5)
https://splunkbase.splunk.com/app/812/
SPLUNK Integration detail: https://www.splunk.com/content/dam/splunk2/pdfs/fact-sheets/splunk-for-f5.pdf

## Slide 30
AddOns (Integrations)

## Slide 31
SNMP
Logging
sFlow
AddOns
Accounting, Visibility
& Reporting
iControl
Skunk Works
Notes: https://support.f5.com/kb/en-us/products/big-ip_analytics/manuals/product/avr-implementations-11-6-0/1.html

## Slide 32
AVR (Availability, Visibility & Reporting)
Provides metrics such as:
Transactions per second,
Server latency
Client latency,
Request throughput
Response throughput,
Sessions. Counts
Can view metrics for:
Applications
Virtual servers,
Pool members,
URLs,
Specific countries,
App traffic details
Transaction counters for:
Response codes,
User agents,
HTTP methods,
Countries
IP addresses
Analytics (also called Application Visibility and Reporting) is a module on the BIG-IP® system that lets you analyze performance of web applications.
AVR also provides remote logging capabilities to consolidate statistics gathered from multiple BIG-IP appliances onto syslog servers or SIEM devices, such as Splunk.

## Slide 33
Does require a system “restart” to provision
Does not count as a “module”
There is no license cost
There is CPU, Disk & Memory impact
AVR Provisioning

## Slide 34
Quick Info
The Apache JMeter™ application is open source software, a 100% pure Java application designed to load test functional behavior and measure performance. It was originally designed for testing Web Applications but has since expanded to other test functions.
http://jmeter.apache.org/

## Slide 35
Couple of iRules
when CLIENT_ACCEPTED { snat [expr int(rand()*255)].[expr int(rand()*255)].[expr int(rand()*255)].[expr int(rand()*254)] virtual avr_vs2 } when HTTP_REQUEST { set my_index [expr int(rand()*10)] set user_agent [class element -value $my_index random_agents] HTTP::header replace user-Agent $user_agent }
when LB_SELECTED { if {([LB::server addr] equals "10.128.20.13") and ([HTTP::uri] equals "/welcome.php")} { after 500 } elseif {[LB::server addr] equals "10.128.20.13"} { after 200 } }
random_agents_ip
server_delay (what?)
This is not the “server team torture device” you have been looking for

## Slide 36
Getting Started – Analytics Profile
Build Analytics Profiles
Assign it to Virtual Server
Start Reporting

## Slide 37
Name
Internal or External Logging
Traffic Capture Logging Type
Notifications
Setting up an Analytics Profile

## Slide 38
Getting Started – Analytics Profile
Metrics
Max TPS & Throughput
Page Load Times
User Sessions
Collected Entities
Very cool pieces of information
Applied Virtual Servers
Caution with
Page Load Times
Injects Java Script which can affect system performance & application functionality
Notes: https://support.f5.com/kb/en-us/products/big-ip_analytics/manuals/product/avr-implementations-11-6-0/4.html

## Slide 39
Applying Analytics Profile to Virtual Server
Change from
“Basic”
to “Advanced”

## Slide 40
AVR Dashboard

## Slide 41
AVR Graphics
Drill into widgets for more details
Particularly the 404 Errors

## Slide 42
AVR Graphics

## Slide 43
STOP: I know what you are thinking
AVR Graphics – My favorite

## Slide 44
Widget Detail – Server Latency
Detailed Information by URL
Avg Server Latency (ms)
Max Server Latency (ms)
View by “Urls”

## Slide 45
Widget Detail – Track 404’s

## Slide 46
Words of Caution …
Its not a historical tool it’s a visibility & troubleshooting tool
Data retention is based on your traffic loads (expect a week)
Its not the be all end all … there are things that could be better
It fills a need. Products like BIG-IQ (management) are intended for larger scale visibility and reporting

## Slide 47
Let’s …

## Slide 48
Provide you & your teams greater visibility
Provide another perspective on your traffic
Put more “information” in your hands
Save you time
Get more value out of your investment – the tools are there … use them

## Slide 49
SNMP
Logging
sFlow
AddOns
Accounting, Visibility
& Reporting
iControl
Skunk Works

## Slide 50
Skunk Works
function f5Data($url) {
$ch = curl_init();
curl_setopt($ch, CURLOPT_URL, $url);
curl_setopt($ch, CURLOPT_SSL_VERIFYPEER, false);
curl_setopt($ch, CURLOPT_HTTPAUTH, CURLAUTH_BASIC);
curl_setopt($ch, CURLOPT_USERPWD, "admin:#######");
curl_setopt($ch, CURLOPT_RETURNTRANSFER, 1);
$response = curl_exec($ch);
$errmsg = curl_error($ch);
$cInfo = curl_getinfo($ch);
curl_close($ch);
return $response;
}

## Slide 51: Looking Forward …
Late June: TCPDump follow-up
Next User Group (BIG-IQ? / ASM?)
Santa Rosa User Group
NewsLetter Feedback
Code train…

## Slide 52: Questions
T

## Slide 53: F5 Overview (Your very brief one slide marketing syllabus)
Publicly traded on NASDAQ
(IPO 1999)
3,300+ employees
Leading provider of application and data delivery networking
160,000+ registered users, geeks, contributors from over 191 countries
Our products sit at strategic points of control in any infrastructure
Industry leading security platform for application delivery and web application firewall
References available upon request
DevCentral
F5 Enterprise Partner Ecosystem
Notes: F5 is the global leader in Application Delivery Networking, and continues to be a solid provider and customer ally as we continue to grow and expand the entire ADC market.

## Slide 54: Thank you for you time…
T